## Slide 1: LAND NAVIGATION

## Slide 2: AGENDA
Definitions
Marginalia
Map colors
Norths
Declination Diagram
Compass techniques
Terrain features
Situational questions

## Slide 3: Knowledge Check
What is the definition of a map?
Where would you find useful information that will help you read a map?
What are the Colors of a Military Map and What do they represent?
How many Norths are on a Military Map?
What does the Declination Diagram display?
What two techniques for using the Lensatic Compass?
What are the Five Major Terrain Features?
What are the Three Minor Terrain Features?
Notes: A graphic representation of a portion of the earth's surface drawn to scale, as seen from above
In the Marginal Information – real answer THE LEGEND & MARGINALIA
Map colors
  Black. Indicates cultural (man-made) features such as buildings and roads, surveyed spot elevations, and all labels.
  Red-Brown. The colors red and brown are combined to identify cultural features, all relief features, non-surveyed spot elevations, and elevation, such as contour lines on redlight readable maps
  Blue. Identifies hydrography or water features such as lakes, swamps, rivers, and drainage
  Green. Identifies vegetation with military significance, such as woods, orchards, and vineyards
  Brown. Identifies all relief features and elevation, such as contours on older edition maps, and cultivated land on red-light
  Red. Classifies cultural features, such as populated areas, main roads, and boundaries, on older maps
Three; true north, magnetic north, and grid north
Shows the angular relationship, represented by prongs, among grid, magnetic, and true norths
The Centerhold Technique // The Compass-to-Cheek Technique
Hill, Valley, Saddle, Ridge, Depression
Cliff, Spur, and Draw

## Slide 4: Situational Questions
You are preparing to conduct a class on land navigation. How will you resource, prepare, and execute this training?
A Soldier is having difficulties in understanding how to read contour lines on a map. How will you teach this Soldier?
During a field exercise you overhear a Soldier complaining about using a lensatic compass saying, “I have a compass on my phone and a government issued GPS”. What is your response?

## Slide 5: Summary
Definitions
Marginalia
Map colors
Norths
Declination Diagram
Compass techniques
Terrain features
Situational questions

## Slide 6: Questions